## Slide 1: Sterilization

## Slide 2
Sterilization:
Is a process by which an article, surface or medium is made free from all micro-organisms either in the vegetative form or spore form.
Disinfection:
Is a process of destruction of vegetative forms of pathogenic organisms which are capable of producing infection but not necessarily resistance to spores.
Antiseptics:
Are substances which are non-toxic for superficial application on living tissues. They prevent the growth and multiplication of microbes.
DEFINITIONS

## Slide 3: Classification Of Sterilization
A. Physical Method
B. Mechanical Method
C. Chemical Method
D. Radiation Method

## Slide 4
A.Physical Method
1.Sunlight
2. Drying
3. Heat
a) Dry heat
i. Flaming
ii. Red heat
iii. Incineration
iv. Hot air oven
b) Moist heat
i. Below 100 deg C
I.Water Bath
II. Vaccine bath
III. Pasteurization
IV. Inspissatioin
ii. At 100 deg C
I. Boiling
II. Tyndallization
III. Steaming
iii. Above 100 deg C
• Autoclave
B. Mechanical Method
Filtration
• Air filter
• Membrane filter
C. Chemical Method
1. Phenols
2. Halogens
3. Alcohols
4. Metallic Salt
5. Aldehydes
6. Gaseous
7. Peroxygens (Oxidizing Agent)
D. Radiation Method
1. Non Ionizing
i. UV rays
ii. Infra rays
2. Ionizing

## Slide 5
  A. Physical Methods
1. Sun Light :
Sunlight has an active germicidal effect due to the combined effect of heat rays and UV rays
One of the natural methods of sterilization in cases of water in tanks, rivers, ponds, lakes etc.
2.Drying :
Moisture is highly essential for bacterial growth.
4/5th of bacterial cell is composed of water, drying is very harmful for bacteria.
Spores are unaffected by drying.

## Slide 6
3. Heat:
  Heat is the most rapid and best method of sterilization.
  It is the method of choice if the material to be sterilized is stable enough to withstand the required temperature necessary to kill the microbes.
  Increasingly elevated temperature are microbicidal but lower temp. usually have static or inhibitory effect.
a. Dry Heat
i. Flaming :
  It involves passing the articles in Bunsen flame without allowing it to become red hot.
  Destroys the vegetative organisms from scalpels glass slides, cover slips, mouth of culture tubes and bottles etc.

## Slide 7
ii. Red heat :
  Items are heated in the Bunsen flame until red hot.
  Used to sterilize Inoculating wire loops and needles.
  This method is for immediate and limited use.
iii. Incineration :
  This is the most common method of treating / destroying infectious waste.
  hazardous materials are burned to ashes at 870 to 980oC.
  used for disposable materials like hospital gowns , soiled dressings , animal carcasses (dead body) , beddings and pathological materials etc are all destroyed by this method.

## Slide 8
iv. Hot air oven :
It is a thermostatically controlled instrument used for the sterilization of certain lab apparatus by the dry heat method.
The best method for the sterilization of glass apparatus such as test tubes and Petri dishes, flasks and metal wares like scissors, forceps etc.
Components of Hot air over:
A double walled aluminum chamber.
A fan for free circulation of hot air within the chamber.
A thermometer and a thermostat for adjusting the required temperature.
Open mesh shelves which can be adjusted.

## Slide 9
Procedure for use:
The articles to be sterilized are dried and wrapped with craft paper and are placed in the oven with enough space in between
The door is firmly closed and the mains are switched on.
The temperature is adjusted to 160▫c and holding period of 1 hour is maintained.
Once the required time is attained, the mains are switched off.
The oven is opened only when it gets cooled (below 40 deg C).
Precautions to be taken
The oven should not be overloaded.
Glass wares should be perfectly dry.
Test tubes and flasks should be plugged with cotton.
Petri dishes, test tubes should be wrapped in craft paper.

## Slide 10
Advantages
Heat can be applied in a controlled manner.
Articles remain dry after sterilization.
Disadvantages:
Long time duration
Not suitable for sterilization of culture media

## Slide 11
b. Moist Heat
i. Moist heat at temperature below 100oC
I. Water bath:
  Sterilization of serum and body fluids in water bath at 56oC for 1 hour.
  Temperature beyond 56oC causes coagulation of serum protein.
II. Vaccine bath:
  Same as water bath but the temperature employed is 60oC for 1 hour.
  Used for sterilizing bacterial vaccines.
  Temperature beyond 60oC loose the potency of vaccine.

## Slide 12
III. Pasteurization :
  Introduced by Louis Pasteur
  Used to sterilize raw milk which may contain Brucella, Salmonella, and tubercle bacilli.
Different methods of Pasteurization.
1. Holder method: 63oC for 30 minutes.
2. Flash method: 72oC for 15-30 Seconds
3. Ultra Pasteurization: 125oC-138oC for2-4 seconds

## Slide 13
IV. Inspissations :
Serum or egg containing media can be sterilized by heating at 80oC - 85oC for 30 minutes on three successive days.
E.g. Loeffler's serum slope, Lowenstein- Jenson media.

## Slide 14
ii) Moist Heat at temperature 100oC
Boiling :
Boiling for 10-30 minutes usually kills all the nonsporing bacteria.
Used to sterilize drinking water and clothes.
Can not be applied to sterilize the surgical instrument as then may contain spores.
II. Tyndallization (Intermittent Sterilization) :
Sterilization is conducted by exposure to free flowing steam at 100oC for 30-60 minutes for 3 successive days.
Generally used to sterilize culture medium containing sugars, gelatin, serum, egg etc. which break down at higher temp.

## Slide 15
III. Steaming :
  This method utilizes steam at 100oC for 5- 10 minutes
  Commonly used for the sterilization of Broth, Nutrient Agar etc.
  Not as effective as autoclaving.

## Slide 16
iii. Moist heat at temperature above 100oC
Autoclave :
Autoclaving is the most reliable and widely used method for sterilization of media and surgical instruments.
Parts:
  Vertical or horizontal tank heated below by gas or electricity.
  Lid with a gasket enabling it to be fitted tightly
  Perforated tray below which water can be poured to a certain level.
  The articles to be sterilized are placed on this tray
  Discharge Tap for air and steam
  Pressure gauze to measure pressure and
  Safety valve.
  Autoclaves Discharge Tap Lid Safety Valve Pressure Gauze

## Slide 17
Operation procedure :
  Adequate amount of water should be added to generate sufficient amount of steam.
  The articles to be sterilized are placed on the perforated tray with enough space left in between for free circulation of steam.
  The lid is placed in portion, discharge tap is opened and the lid is screwed down.
  The heater is put on.
  Water begins to boil and a mixture of steam and air escape through the discharge tap freely.
  When all the air is removed from the autoclave and a constant jet of steam comes out, the discharge tap is closed.
  The pressure gauze indicates that required pressure is reached and an automatic regulator maintains a constant pressure of 15lbs.

## Slide 18
At 15lbs pressure, temp of 121oC can be obtained. Thus at a temperature of 121oC (15lbs) , a holding period of 15 minutes of maintained.
The heating element is switched off and the autoclave is allowed to cool, till the pressure comes back to zero.
The discharge tap is opened and air is allowed to enter into it slowly.
Examples of articles which can be sterilized by autoclave
All rubber articles (except silicon rubber) ,Glass metal syringes , Basal culture media ,Discharged bacterial cultures, Clothes and glove powders ,Certain lab instruments etc.

## Slide 19
B. Mechanical Methods :
  This method uses filtration.
  Filtration is the Removal of microbes by passage of a liquid or gas through a screen like material with small pores.
  Used to sterilize heat sensitive materials like vaccines, enzymes, antibiotics, and some culture media.
  High Efficiency Particulate Air Filters (HEPA): Used in operating rooms and burn units to remove bacteria from air.
  Membrane Filters: Uniform pore size. Used in industry and research. Different sizes:
0.22 and 0.45um Pores: Used to filter most bacteria. Don’t retain spirochetes, mycoplasmas and viruses.
0.01 um Pores: Retain all viruses and som e large proteins.

## Slide 20
C. Chemical Methods
  Phenols and Phenolics:
    Active microbicidal agent
    Used to decontaminate infective discharges, bed pans, hospital floors.
Advantages: Stable & persist for long times after applied.
2. Halogens:
    Common halogens in use are iodine, chlorine or chlorine compounds.
    Effective alone or in compounds.

## Slide 21
A. Iodine:
i) Tincture of iodine:
  was one of first antiseptics used.
  Stains skin and clothes, somewhat irritating.
ii) Iodophors:
  Used as skin antiseptic in surgery. Not effective against bacterial endospores.
  Betadine
  Isodine
B. Chlorine:
  Exists as gas in chemical form.
  When mixed in water forms hypochlorous acid:
Cl2 + H2O ------> H+ + Cl- + HOCl
Hypochlorous acid
  Used to disinfect drinking water, pools, and sewage.

## Slide 22
3. Alcohols:
  Kill bacteria, fungi, but not endospores or naked viruses.
  Act by denaturing proteins and disrupting cell membranes.
  Evaporate, leaving no residue.
  Used to mechanically wipe microbes off skin before injections or blood drawing.
  Not good for open wounds, because cause proteins to coagulate.
  Ethanol: Optimum concentration is 70%.
  Isopropanol
  Methanol

## Slide 23
4. Metallic Salts:
  Include copper, selenium, mercury, silver, and zinc.
  Very tiny amounts are effective.
  Silver:
    1% silver nitrate used to protect infants against gonorrheal eye infections.
B. Mercury:
    Organic mercury compounds like merthiolate and mercurochrome are used to disinfect skin wounds.
C. Copper :
    Copper sulfate is used to kill algae in pools and fish tanks.

## Slide 24
D. Selenium:
  Kills fungi and their spores.
  Used for fungal infections.
  Also used in dandruff shampos.
E. Zinc
  Zinc chloride is used in mouthwashes.
  Zinc oxide is used as antifungal agent in paints.

## Slide 25
5. Aldehydes:
  Formaldehyde gas:
    Commonly used as formalin, a 37% aqueous solution.
    Formalin was used extensively to preserve biological specimens and inactivate viruses and bacteria in vaccines.
    2-5% Formaldehyde vapor uses for fumigation of rooms.
    Irritates mucous membranes, strong odor.
B. Glutaraldehyde:
    Less irritating and more effective than formaldehyde.
    A 2% solution of glutaraldehyde (Cidex) is Commonly used to disinfect hospital instruments like arthroscopes, bronchoscopes.

## Slide 26
6. Gaseous Sterilizers:
Ethylene Oxide:
  Used to sterilize temperature sensitive materials.
  Kills all microbes and endospores, but requires exposure of 4 to 18 hours.
  Highly penetrating
  Toxic and explosive in pure form.
7. Peroxygens (Oxidizing Agents):
Hydrogen Peroxide (33%):
  Used as an antiseptic but Not good for open wounds because quickly broken down by catalase present in human cells.
  Effective in disinfection of inanimate objects.
  Used by food industry and to disinfect contact lenses.

## Slide 27
D. Radiation method
Non-ionizing radiation
a. UV rays:-
  Electromagnetic radiation with wavelength 100-400 nm .
  The rays of wavelength between 240 and 280 are absorbed by nucleic acids that alter the structure of the DNA and leads to the death of the cell.
  UV radiation do not penetrate glass, opaque solids or liquids.
  Generally used in work areas such as media pouring rooms, safety cabinets or air in surgical rooms.
  UV rays should not be allowed to come in contact to the eyes.

## Slide 28
b. Infra red radiation :
  Wavelengths longer than those of visible light.
  Kills micro organisms by oxidation as a result of heat generated (form of hot-air sterilization).
  Ideal for sterilizing a large number of articles such as syringes in a short time.
  Sterilization is done at 190oC for 10 minutes.

## Slide 29
2. Ionization Radiation:
  Unlike UV radiation, ionization radiation penetrates non-living and living organism.
  Sterilization is achieved without appreciable rise in temperature so also referred as 'cold sterilization’.
  To sterilize heat sensitive medical supplies such as plastic syringes, drugs etc .
  Cathode rays and gamma rays are the most effective ionizing radiation.
  These rays are highly expensive and dangerous.